## Slide 1: Data Assimilation Summer School Romania, 2025
Jo Eidsvik
Department of Mathematical Sciences,
NTNU, Norway
Jo.Eidsvik@ntnu.no

## Slide 2: Plan
Time | Topic
Lecture 1 | Bayesian model updating
 | State space models
Lecture 2 | Design of experiments
 | Decision analysis and the value of information
Lecture 3 | Informative sampling designs in space-time
 | Examples with AUV surveying in the ocean
Lecture 4 | Value of information analysis / Sequential information gathering
 | Examples with CO2 storage monitoring in the subsurface
https://joeid.folk.ntnu.no/Romania25/

## Slide 3: Bayesian model
All the currently available information about variables:
New data (and the data gathering scheme) is represented by a likelihood model:
If we collect data, the model is updated to the posterior, conditional on the new observations:

## Slide 4: Adaptive sampling – with sequential data assimilation
.
Collect data over time.
Always choose best design for data gathering.
Update model with data.
Select the data design according to highest expected reward.
Do so at each stage.

## Slide 5: Optimal sequential design
.

## Slide 6: Strategy for information gathering
.
Find best first data design, if any sufficiently informative.
Collect first data using best design.
Update probability distributions, conditional on the data.
Find second best design, in new model, if any sufficiently informative.
Collect second data (by simulation from new model) using best design.
Update probability distributions, conditional on the data.
Find third best data, in new model, if any sufficiently informative.
.....
1 level
2 level
3 level
…..

## Slide 7: Adaptive sampling – greedy or optimal
.
The exact solution to sequential data gathering is only available in small-size discrete models. (It becomes a combinatorial problem)
Various approximate strategies exist. (Approximate dynamic programming).
Myopic (near-sighted) is a common strategy for sequential problems.
It considers only one stage at a time, not looking into the ‘future’:
(A heuristic solution to the dynamic program.)

## Slide 8
AUV objectives – adaptive sampling
TASKS:
Where and when should autonomous underwater vehicle (AUV) go to collect valuable data?
AUV
AUV must have an onboard statistical model, which is relatively easy to update in real-time. (Limited computer resources.)
AUV must be embedded with a set of possible designs and a criterion for wise data gathering. (It cannot communicate much.)
AUV must be controlled to operate on a set of changing tasks to achieve its goals. (AI in practice.)
Lots of other related examples. IoT, embedded systems, smart sensors, etc.

## Slide 9: Data collection assumption – waypoint graph
Survey design for AUV is restricted to a waypoint graph.
Design can be static (pre-planned) survey lines on the waypoint graph:
Lawnmower
Space-spanning designs.
Or one can do sequential (adaptive) designs, where one updates the sampling plan based on what has been seen so far.

## Slide 10
Relevance:
Plankton : ‘every (2nd) breath you take’
ChlA : multispectral image from satellite.
- Satellite data are coarsely sampled, and influenced by clouds.
- Numerical ocean models are often biased over long spatio-temporal scales.
- Buoy data are only at a few locations.
- Traditional data gathering by ships is expensive.
Autonomous vehicles can improve the current state of sampling the ocean.

## Slide 11
Relevance: Algal bloom
One can sometimes ‘see’ this from satellite data.
Better monitoring efforts could help mitigate such events in the future.
Autonomous vehicles can improve the current state of sampling the ocean.

## Slide 12: Effective mapping of river plume front
Nidelva river, Trondheim, Norway.
Fresh cold water from river runs into the fjord.
Goal is to combine spatial statistics and marine robotics to suggest designs that efficiently minimize the expected ‘uncertainty’ associated with the river plume water masses.

## Slide 13: Gaussian prior and likelihood
Gaussian spatial process prior (learned from current knowledge).
Likelihood, design matrix, picks data locations, for every time step.

## Slide 14: Gaussian prior and likelihood
Gaussian spatial process prior (learned from current knowledge).
Likelihood, design matrix, picks data locations, for every time step.
We will select this intelligently over time.

## Slide 15
Criterion - Excursion sets
Locations where the variable is below a threshold.

## Slide 16
(Bivariate) excursion sets

## Slide 17
Myopic path selection for excursions
Real time excursion probability (blue = cold fresh water, yellow = salt warm water.

## Slide 18
Excursion sets and excursion probabilities
Criterion for path selection (at every sampling stage):
Closed form for Gaussian variables.
Multivariate Gaussian cumulative distribution functions.
No data:
With data:

## Slide 19: Conditional mean and covariance
We do updating along transects, on a waypoint graph of possible AUV designs.
Gaussian model enables fast onboard calculations (AUV has a computing unit).

## Slide 20
Myopic path selection for excursions
Illustration in a simulation study

## Slide 21: Field experiment - mapping plume in 3D
Fresh cold water from river runs into the fjord.
Nidelva river, Trondheim, Norway.

## Slide 22
3D Ocean model of Nidelva river
Fit a prior model from numerical ocean model ‘data’. SINMOD developed by Sintef.

## Slide 23
3D monitoring with AUV
0.5 m depth

## Slide 24
3D GMRF model
3D Gaussian Markov Random Field (GMRF) is fit ahead of the operation, using SINMOD data.
Goals:
More realistic covariance function. Basis functions in covariance (precision matrix) parameterization are estimated from SINMOD ocean model data.
Using the 3D GMRF model for efficient sparse matrix-vector calculations, onboard the AUV. This scales much better for large 3D grids.
Predicted excursion set during survey.

## Slide 25: Exercise: Sequential VOI in Gaussian models
Consider again the 25x25 grid, with a Gaussian process prior for profits
(like in a forestry example).
Assume the decision situation where one makes decisions on the sum of mean values over all cells on the grid.
Use the myopic strategy to find sequential data designs along the 25 East-West lines. The price of a test is P=0.1.
How many tests are done before we stop? (varies with data samples)
What tests are usually done? (varies with data samples)
By playing the game over many runs, we can study properties of the approach.
https://joeid.folk.ntnu.no/Romania25/SeqLinesGP.py

## Slide 26: Exercise: Sequential VOI in Gaussian models
First design is line 13.
Resource: forest values in each grid node.

## Slide 27: Myopic scheme for survey line sampling
.
Find best single survey line, if any.
Collect data for this line.
Update the model
Stop testing or continue testing.
Etc….
Find largest among all design lines j.

## Slide 28: Exercise: Sequential VOI in Gaussian models
First design is line 13.

## Slide 29: Exercise: Sequential VOI in Gaussian models
First design is line 13.

## Slide 30: Exercise: Sequential VOI in Gaussian models
This run stops after 3 steps because the decision was easy to make : harvest.

## Slide 31
RRT* algorithm for long-horizon planning.
GRF updating.
AUV has an objective function with a mix of criteria, and must get ‘home’ in time.
Non-myopic sampling

## Slide 32
Results
Trondheimfjord

## Slide 33
Other application – space-time excursion
(pollution monitoring in Norwegian fjord)

## Slide 34
Space-time model and sampling
Diffusion-advection SPDE model represent the complex differential equations rather well.
Discretized to a state-space model for the Gaussian random field in 2D.
This is updated onboard in real-time, using similar closed form calculations for design.

## Slide 35
Space-time sampling and Error reduction

## Slide 36
Sampling for hot-spots in Chlorophyll A
Adaptive AUV sampling to explore for large values (hotspots) of Chlorphyll A.
Criterion: Go for places that are expected to be hotpots and have large variance.

## Slide 37
Sampling for hot-spots in Chlorophyll A
Improvement and expected improvement:
Largest sampled so far
Choose path with largest expected improvement (at each stage):

## Slide 38
Expected improvement sampling

## Slide 39
Mission Western Norway
Starts by going to maximum depth, then adapts according to expected improvement criterion.

## Slide 40
Mission Western Norway

## Slide 41
Mission Western Norway
– links to zooplankton

## Slide 42
Mission Western Norway
– links to zooplankton