## Slide 1: Data Assimilation Summer School Romania, 2025
Jo Eidsvik
Department of Mathematical Sciences,
NTNU, Norway
Jo.Eidsvik@ntnu.no

## Slide 2: Plan
Time | Topic
Lecture 1 | Bayesian model updating
 | State space models
Lecture 2 | Design of experiments
 | Decision analysis and the value of information
Lecture 3 | Informative sampling designs in space-time
 | Examples with AUV surveying in the ocean
Lecture 4 | Value of information analysis / Sequential information gathering
 | Examples with CO2 storage monitoring in the subsurface
https://joeid.folk.ntnu.no/Romania25/

## Slide 3: Value of information (VOI)
Prior value:
Posterior value:
- Uncertainties
- Alternatives
- Data
- Value function
VOI = Expected posterior value – Prior value

## Slide 4
Computation - Formula for VOI
Main challenge.

## Slide 5: Approximate computation
Suggest Monte Carlo (outer) and regression approximation (inner).
Inner expectation:
Outer expectation:

## Slide 6: Simulation-regression illustration
Build regression model from Monte Carlo samples.
Sample variables from prior.
Sample data from likelihood.
Set alternatives.
Evaluate value function.

## Slide 7: Simulation-regression algorithm
Inner expectation
Outer expectation
Simulate uncertainties:
Compute values, for all alternatives:
Simulate data:
Regress samples to fit conditional mean:

## Slide 8
Illustration - fit regression model to samples

## Slide 9
Illustration - fit regression model to samples

## Slide 10
.
Choice of regression method
Linear regression
Principal component regression
Neural networks
K-nearest neighbors
And many others
Cross-validation to check model fit. Look at residuals

## Slide 11
Exercise - two different cases
In both displays:
Alternative 1,
Alternative 2
for which of these two cases is the VOI largest.

## Slide 12: Petroleum example - infill drilling
Decisions about infill drilling for improved oil recovery.
  - Uncertainty, heterogeneity and dependence make this choice difficult.
Data gathering decisions about time-lapse seismic data.
  - Which kind of data are likely to be valuable? How much data is enough?
Wells drilled at the Gullfaks field, North Sea.
Well data
Geological knowledge
time
Production
Time lapse seismic
Baseline seismic
Infill drilling

## Slide 13: Illustration of values and data influence
Infill drilling (Alternative 1) can give more value, but can also mean loss.
If data indicate reservoir variables corresponding to these high values
-> do infill drilling!
If data indicate reservoir variables corresponding to these small values
-> avoid infill drilling!
… such data would lead to better decisions in this situation.

## Slide 14
.
Is VOI larger than price of time-lapse seismic experiment?
Is VOI larger for seismic acquisition design A or B ?
Is VOI larger for seismic processing type I or II ?
Information gathering and VOI
VOI is interpretable as follows:
VOI = Expected posterior value – Prior value

## Slide 15: Gullfaks case (infill drilling and time lapse)
Time-lapse seismic has shown useful at Gullfaks. But no formal VOI analysis was conducted up-front.
We consider this case in retrospect.
Well data
Geological knowledge
time
Production
Time lapse seismic
Baseline seismic
Infill drilling
5 decision alternatives.

## Slide 16
Prior - Reservoir uncertainty
This distribution of reservoir variables is represented by multiple Monte Carlo realizations (ensembles) from the prior distribution.
Sample 1
Sample 1000
………….
Prior is .
Uncertainties: saturation, pressure, porosity, permeability and fault transmissibilities. (Conditioned on existing data.)

## Slide 17: Simulation-regression illustration
Build regression model from Monte Carlo samples.
Sample reservoir variables.
Sample data from likelihood.
Set alternatives.
Evaluate value function.

## Slide 18: Gullfaks case (values)
Future production for 5 different infill drilling alternatives.
- for each realization, all alternatives are «produced».

## Slide 19: Simulation-regression illustration
Build regression model from Monte Carlo samples.
Sample reservoir variables.
Sample data from likelihood.
Set alternatives.
Evaluate value function.

## Slide 20: Gullfaks case (likelihood of AI data)
Synthetic time-lapse seismic (acoustic impedance (AI) proessing):
Use rock physics relations connecting reservoir properties to AI.
Simulations indicate some information about saturation from AI for this case.

## Slide 21: Gullfaks case (likelihood of R0,G data)
Synthetic time-lapse seismic (processing more angle information (R0,G)):
Use rock physics relations connecting reservoir properties to (R0,G).
Simulations indicate limited information about saturation from (R0, G).

## Slide 22: Simulation-regression illustration
Build regression model from Monte Carlo samples.
Sample reservoir variables.
Sample data from likelihood.
Set alternatives.
Evaluate value function.

## Slide 23
.
Large data: Partial least squares regression
Partial least squares (PLS) regression is used for regression values on large seismic data set.
Cross-validation to find optimal number of linear combinations.
PLS is similar to Principle component regression (PCR).
(PLS focuses on explaining covariance instead of variance.)
Number of regressors
Prediction residual
(cross-validated)

## Slide 24: Gullfaks case (PLS for expected values)
Fit regression model from Monte Carlo samples.
12 regressor components in the PLS regression.

## Slide 25: Gullfaks case (predictive power)
Fit of regression models is reasonable (based on AI data here).

## Slide 26: Gullfaks case (VOI results)
Acoustic impedance (AI)
Angle information, (R0,G)
VOI of time-lapse data is about $50 million.
No big differences in VOI of processing methods
(but the price of these likely differ).
(Bootstrap used to get distribution.)

## Slide 27
Examples of CO2 monitoring
Smeaheia prospect
(uncertainty in fault migration)

## Slide 28: CO2 monitoring
Monitor when the
uncertainty is larger?
risk of leakage exceeds limit?

## Slide 29
Examples of CO2 monitoring
Sleipner storage
(migration from pressure and chimneys)
2025 Full Waveform inversion results

## Slide 30: Flow experiment, Sleipner model

## Slide 31: Airflow simulations
Simulation based on diffusion principle and gravitational forces

## Slide 32
Invasion percolation
Markovian structure.

## Slide 33
Illustration Invasion percolation
Injection of CO2
Migration
Layer
Layer
Layer
Migration from layer if:
Notes: We consider a stratigraphic model having m layers of high porosity and permeability rock, separated by cap rocks having lower permeability. We assume that CO2 is injected in the bottommost layer. Now we attempt to model the volumes and pressures in each layer with time based on the invasion-percolation concept. The CO2 volume in the first layer increases with time, which increases the height of the CO2 column in that layer and so the pressure increases with time as well. When the pressure reaches the capillary threshold pressure of the cap rock above, CO2 starts leaking to the second layer. CO2 then keeps accumulating in the second layer until the pressure reaches the capillary threshold pressure for its cap rock, at which point it will migrate to the layer above. This process keeps repeating until CO2 finally leaks from the topmost layer.

## Slide 34
Assumptions of Invasion Percolation model
CO2 column height:
Capillary pressure threshold: Depends on cap rock properties.
Migration from layer j if:
Depends on geometric conditions of formations.
Known CO2 volumes are injected over time .
End time
Volumetric pressure: is difference in density between CO2 and brine.
Notes: Here are the assumptions of the invasion percolation model. We assume that we plan to inject a known volume of CO2 for a total time period of T. The CO2 column height in any layer j at any point of time is some function of the volume of CO2 in that layer. This function will depend on the geometry of the formation. Then, the volumetric pressure is a deterministic function of the height of the CO2 column. The capillary pressure threshold for each cap rock depends on its properties like permeability. And finally, migration from one layer to the layer above will happen if and when the pressure in that layer reaches the capillary threshold pressure of its cap rock.

## Slide 35
Stochastic model – fit to Sleipner formations
Capillary pressure thresholds:
Volumes of CO2:
Volume to height transform (depends on geometry of formation):
where is rate of injection,
is time of migration from layer.
(for ellipsoidal cap model)
Times of migration:
Or,
So,
(for ellipsoidal cap model)
Notes: Based on the invasion-percolation concept, we build a stochastic model to simulate various parameters. We assume that the capillary pressure threshold for each layer is random and distributed according to a log normal distribution. The volume of CO2 in each layer depends on the rate of injection and the time of migration, which is deterministic given the capillary pressure thresholds. To determine the heights of the CO2 column from the volumes, we use a transform which depends on the geometry of the formation. In this work, we use this equation which is derived from an ellipsoidal cap model. Here a, b and c are axes of the ellipsoid from which the ellipsoidal cap has been extracted. Then, we can derive a relation between time and height, which can be used to find the heights of the CO2 column at any point of time. Finally, to determine the time of migration for each layer, we need to equate the pressure in that layer with the capillary threshold pressure for that layer, and find the time at which this condition is satisfied.

## Slide 36: Migration times - Sleipner
Notes: After we have modeled the key components of VOI, we can evaluate the VOI using the equation shown here. The VOI is defined as the difference between the posterior value with information and the prior value without information. The prior value is given by the maximum expected value over the spatial uncertainty X, the maximization performed over the possible alternatives a. But if we have information before making our decision, we can choose the optimum alternative for each information outcome. So the max goes inside the integration for the posterior value. However, since the VOI is calculated before actually collecting the information, we do not know what information outcome we would observe, and so we need to take the expectation over all possible information outcomes. The information is usually not perfect and so it gives us a distribution of X conditioned on the information Y. Finally, since the reservoir properties X are very high dimensional, we approximate the distribution of X using an ensemble of realizations, and then the integrations reduce to summations over the realizations.

## Slide 37
Monitoring by seismic traveltime data indicating column heights
Processing seismic traveltime data to get heights, in each layer j=1,…,m
Question is to find a good survey time t.
Monitoring efforts that are informative and worth the price of acquiring and processing data.
where is the monitoring time,
is the noise term,
is the threshold height that can be detected.
Notes: Now, we can use the stochastic model to estimate the value of information in CO2 storage. Here, we assume that we can get information about the heights of the CO2 column in each layer. To model the imperfect data, we add some noise to the heights, and assume that the heights can be detected only if they are greater than a certain threshold height. The question here is to find a good survey time t at which the data would be highly valuable. The data should be informative as well as worth the cost of acquiring and processing it. To answer this question, we use value of information, which is a decision-analytic metric that quantifies the value that information adds to any decision situation.

## Slide 38: Computing the prospect values
Value of continuing injection:
Value of stopping injection:
where Cost of injection per volume
Cost of leakage per volume
Cost of tax per volume
Rate of injection
End time of injection
Time of leakage
Notes: These are the equations that I used for computing the prospect values. The value of continuing injection at any point of time is equal to the cost of CO2 injection for the remaining time, plus the cost of possible leakage. On the other hand, the value of stopping injection at any point of time is equal to the tax that has to be paid for the CO2 not injected.

## Slide 39
Value of information gained by monitoring
a
αj,βj,γj,Cj
Value
yj
Regress simulated value and simulated data to estimate the Value of Information
Decision alternatives
(Stop or Continue)
Cost of injection,
Cost of leakage,
Cost of not injecting CO2
Model parameters
Notes: To compute the value of information, we use a technique called simulation-regression, in which the prospect values and the data are first simulated and then regressed. This diagram shows the various parameters in the decision situation, and their dependencies. We assume there are two decision alternatives at any point of time – to stop the injection, or to continue. The prospect values would depend on the decision alternative chosen, as well as on parameters like the heights and the capillary threshold pressures. The values should account for the cost of injection, the cost of possible leakage, and the cost of not injecting CO2. As mentioned in the previous slide, the data are simulated from the heights of the CO2 columns by adding random noise terms. And finally, we regress the simulated values on the simulated data to compute the value of information.

## Slide 40: Computing the VOI : simulation-regression
Regress the simulated values on the simulated data to fit and . They approximate the conditional expectations.
Compute Prior Value,
Compute Posterior Value,
Compute the Value of Information,
Notes: These are the steps involved in computing the value of information by simulation-regression. First, we need to regress the simulated values on the simulated data to obtain a regression model, and use that to find the fitted values of continuing and stopping. Then, we find the prior value using this equation. The prior value is essentially the expected value of the alternative which has the maximum expected value. On the other hand, to compute the posterior value, we first take the maximum value for each sample, and then take the expectation. That is because, if we have data, we can choose the alternative with the highest value for each sample. And finally, the value of information is the difference between the posterior value and the prior value.

## Slide 41: Results
Scatter plots of true values and fitted values at t = 16 years
Low noise data
(correlation coefficient = 0.69)
High noise data
(correlation coefficient = 0.66)
VOI = $2.6 million
VOI = $1.6 million
Notes: These plots show how well the fitted values match the true values at t=16 years. For the perfect data, the correlation coefficient is 0.74, while it is 0.69 for the low noise data.

## Slide 42: VOI Results
Notes: So, I computed the VOI for different times of survey and this figure shows the results. We can see that the VOI is very low until about 14 years, at which point it suddenly increases and reaches a peak at about 17 years. There is another somewhat smaller peak at around 28 years. If you remember the distributions of the migration times, the time of migration from the second layer to the third peaks at around 20 years, and the time of leakage from the third layer peaks at around 30 years. So, the peak times in the VOI seem to indicate that there is high value in monitoring before the CO2 migrates from the second layer to the third, and before it leaks from the third layer. On the other hand, there is not much value in monitoring it at early times, which might be because it does not influence the prospect values a lot.

## Slide 43: Sequential VOI over many monitoring stages
Earlier data influence the subsequent data gathering.

## Slide 44: Exercise : best monitor time
Consider a single layer for CO2 injection.
Storage is less expensive than paying tax for other storage sites.
But potential migration has large cost.
What is the best monitoring time?
Data assimilation effects
Notes: So, I computed the VOI for different times of survey and this figure shows the results. We can see that the VOI is very low until about 14 years, at which point it suddenly increases and reaches a peak at about 17 years. There is another somewhat smaller peak at around 28 years. If you remember the distributions of the migration times, the time of migration from the second layer to the third peaks at around 20 years, and the time of leakage from the third layer peaks at around 30 years. So, the peak times in the VOI seem to indicate that there is high value in monitoring before the CO2 migrates from the second layer to the third, and before it leaks from the third layer. On the other hand, there is not much value in monitoring it at early times, which might be because it does not influence the prospect values a lot.

## Slide 45: Exercise: best monitor time
Value of continuing injection:
Value of stopping injection:
where Cost of injection per volume
Cost of leakage per volume
Cost of tax per volume
Rate of injection
End time of injection
Time of leakage
https://joeid.folk.ntnu.no/Romania25/CO2singleLayerDA.py
Notes: So, I computed the VOI for different times of survey and this figure shows the results. We can see that the VOI is very low until about 14 years, at which point it suddenly increases and reaches a peak at about 17 years. There is another somewhat smaller peak at around 28 years. If you remember the distributions of the migration times, the time of migration from the second layer to the third peaks at around 20 years, and the time of leakage from the third layer peaks at around 30 years. So, the peak times in the VOI seem to indicate that there is high value in monitoring before the CO2 migrates from the second layer to the third, and before it leaks from the third layer. On the other hand, there is not much value in monitoring it at early times, which might be because it does not influence the prospect values a lot.