## Slide 1: Value of Information Analysis in Spatial Models
Jo Eidsvik
Jo.eidsvik@ntnu.no

## Slide 2: Plan for course
Time | Topic
Monday | Introduction and motivating examples
 | Elementary decision analysis and the value of information
Tuesday | Multivariate statistical modeling, dependence, graphs
 | Value of information analysis for dependent models
Wednesday | Spatial statistics, spatial design of experiments
 | Value of information analysis in spatial decision situations
Thursday | Examples of value of information analysis in Earth sciences
 | Computational aspects
Friday | Sequential decisions and sequential information gathering
 | Examples from mining and oceanography
Every day: Small exercise half-way, and computer project at the end.

## Slide 3
Geostatistics (Kriging)
What is the value of this additional information?
Is mining profitable?

## Slide 4: Joint pdfs
There are families of joint pdfs. Parametrically, or non-parametrically.
Gaussian distribution is very common:
For a Gaussian process, in a spatial application, the covariance entries are formed in a particular way.

## Slide 5: Spatial covariance functions
Model | Covariance
Exponential | 
Matern 3/2 | 
Cauchy-type | 
Gaussian | 

## Slide 6: Example - Gaussian process
Model | Covariance
Exponential | 
Matern 3/2 | 
Cauchy-type | 
Gaussian | 
Design matrix:

## Slide 7: Gaussian process - model
Goal is:

## Slide 8: Norwegian wood - forestry example
.
Where to put survey lines for timber volumes information?
Typically partial, imperfect information.
Farmer must decide whether to harvest forest, or not. There is uncertainty about timber volumes and profits over the spatial domain.
Another decision is whether to collect data before making these decisions.
If so, how and where should data be gathered.

## Slide 9: Norwegian wood - posterior
Goal is:
Design matrix:
This is Kriging prediction and associated variance.

## Slide 10: Norwegian wood – posterior results

## Slide 11: Norwegian wood – information
We can base data gathering schemes on different criteria
Maximum variance reduction
Maximum entropy
Value of information (VOI)
VOI is based on decision situation!
Others are not material – not tied to decision situation.

## Slide 12: Spatial design
Geometric criterion (space-filling design).
  Minimize average distance between data locations.
  Set a threshold on minimum distance to nearest data location.
Challenging to compare various data accuracies.
Variance reduction criterion.
Kriging-related criteria (slope and weight of mean).
Entropy reduction criterion.
Prediction error.

## Slide 13: Variance reduction
Expected variance reduction:
Could use a weighted sum, or choose a subset of variables for prediction.

## Slide 14: Variance reduction (Kriging)
Overall variance reduction is larger for the random design.

## Slide 15: Other criteria tied to Kriging
Slope of regression : Regression between the predicted and true (block) variables.
Weight of the mean : The relative impact (for blocks), of regression versus that of Kriging.
Test function:

## Slide 16: Entropy (Shannon)
Expected mutual information:

## Slide 17: Entropy of a Gaussian
Very commonly used in the design of spatial experiments (air quality monitoring, river monitoring networks, etc.)

## Slide 18: Entropy of a Gaussian
Compute the entropy of a bivariate standard Gaussian (with no correlation).
Adjust the correlation so that a Gaussian bivariate model with variance equal to 1.5 gets the same entropy as the standard Gaussian in 1..
Exercise:

## Slide 19: Entropy blind-spot
This criterion always looks for marginals with largest entropy!
For a single observation, entropy would select node 1!
1
2
3
4
n

## Slide 20: VOI - Pyramid of conditions
Pyramid of conditions - VOI is different from other information criteria (entropy, variance, prediction error, etc.)
ECONOMIC

## Slide 21
Formula for VOI

## Slide 22
Formula for VOI
Spatial alternatives.
Spatial uncertainties.
Spatial value function.
Spatial data.

## Slide 23: Information gathering
.
 | Perfect | Imperfect
Total | Exact observations are gathered for all locations. This is rare, occurring when there is extensive coverage and highly accurate data gathering. | Noisy observations are gathered for all locations. This is common in situations with remote sensors with extensive coverage, e.g. seismic, radar, satellite data.
Partial | Exact observations are gathered at some locations. This might occur, for instance, when there is careful analysis of rock samples along boreholes in a reservoir or a mine. | Noisy observations are gathered at some locations. Examples include hand-held (noisy) meters to observe grades in mine boreholes, electromagnetic testing along a line, biological surveys of species, etc.

## Slide 24: Decision situations and values
.
 | Assumption: Decision Flexibility | Assumption: Value Function
Low decision flexibility; Decoupled value | Alternatives are easily enumerated | Total value is a sum of value at every unit
High decision flexibility; Decoupled value | None | Total value is a sum of value at every unit
Low decision flexibility; Coupled value | Alternatives are easily enumerated | None
High decision flexibility; Coupled value | None | None

## Slide 25: Decoupling – values are sums
.
 | Assumption: Decision Flexibility | Assumption: Value Function
Low decision flexibility; Decoupled value | Alternatives are easily enumerated | Total value is a sum of value at every unit
High decision flexibility; Decoupled value | None | Total value is a sum of value at every unit
Low decision flexibility; Coupled value | Alternatives are easily enumerated | None
High decision flexibility; Coupled value | None | None
Profit is sum of timber volumes from units.

## Slide 26: Low versus high decision flexibility
.
High flexibility:
Farmer can select individual forest units.
Low flexibility:
Farmer must select all forest units, or none.

## Slide 27: Decoupled versus coupled value
.
Value decouples to sum over units.
Value involves complex coupling of drilling strategies, and reservoir properties.
Petroleum company must decide how to produce a reservoir.
Farmer must decide whether to harvest at forest units, or not.

## Slide 28
Computation - Formula for VOI
Computations :
Easier with low decision flexibility ( less alternatives).
Easier if value decouples (sums or integrals split).
Easier for perfect, total, information (upper bound on VOI).
Sometimes analytical solutions. Otherwise approximations and Monte Carlo.

## Slide 29
Formula for total perfect information
Upper bound on any information gathering scheme.

## Slide 30
I love rock and ore – mining example
What is the value of this additional information?
Is mining profitable?

## Slide 31: VOI workflow
Low decision flexibility. De-coupled value function.
Gather information by XRF or XMET in boreholes. No opportunities for adaptive testing.
Model is a spatial Gaussian process.
VOI analysis done by exact, Gaussian, computations.

## Slide 32: Decision situation and data
Mining blocks. Some waste rock. Some high-grade.
Planned boreholes.

## Slide 33: Information gathering
Planned boreholes.
Total test : 265 measurements in 21 new boreholes.
Partial test: Drilling and sampling data only in a subset of boreholes.
Perfect testing (XRF: done in lab). Imperfect testing (XMET: handheld meter).

## Slide 34: Prior model

## Slide 35: Model

## Slide 36: Prior and likelihood model
Defined by design of boreholes.
Defined by test (XRF, XMET).
Set from current data.
-XRF data
-XMET data

## Slide 37: Results for design
Comparing designs over different criteria:
All, 5 or 10 boreholes
XRF or XMET data
Geometric criterion,
Variance reduction,
Slope,
Weight of mean,
Entropy,
VOI,

## Slide 38: Results
Relative criterion | Geometric | Krig Std | Slope | Weight | Ent | VOI
5 XRF / All XMET | 0.88 | 0.87 | 0.87 | 0.84 | 0.76 | 0.39
5 XRF/ All XRF | 0.88 | 0.85 | 0.82 | 0.81 | 0.41 | 0.27
10 XRF / All XMET | 0.94 | 0.96 | 0.97 | 0.95 | 1.21 | 0.94
10 XRF / All XRF | 0.94 | 0.93 | 0.91 | 0.91 | 0.72 | 0.64
All XRF / All XMET | 1 | 1.03 | 1.07 | 1.04 | 1.68 | 1.45
All XRF / All XRF | 1 | 1 | 1 | 1 | 1 | 1

## Slide 39
VOI
Analytical solution under the Gaussian modeling assumptions.
Weights set from block model(waste or ore).

## Slide 40: VOI : Decision regions XRF,XMET.

## Slide 41: VOI : Decision regions, partial data.

## Slide 42: Take home from this exercise:
.
Information connected to partial perfect testing can be less/more than total imperfect testing.
Information criteria depend on design and data accuracy.
Entropy appears to like perfect information.
VOI can be connected with decisions and prices (not so easy for other criteria).

## Slide 43: Norwegian wood - forestry example
.
Where to put survey lines for timber volumes information?
Typically partial, imperfect information.
Farmer must decide whether to harvest forest units, or not.
Another decision is whether to collect data before making these decisions.
If so, how and where should data be gathered.

## Slide 44: Design
.
Where to put survey lines for timber volumes information?
Typically partial, imperfect information.
Design matrix:
Picks the measurement locations for a partial test.
Total test.
Example of imperfect test.

## Slide 45: Three different designs
.
Survey lines for timber volumes information?
Three data designs:
Total (all cells)
Partial (all cells along center lines)
Aggregate partial (sums along the two center lines).

## Slide 46: Gaussian process for value
Motivation, uncertainties on a grid - model profits directly
(normalized for area).
Forest units.
Uncertainty is value in each cell.
Global alternatives
Local alternatives

## Slide 47: Prior is Gaussian process
.
Spatial dependence,
Matern covariance.

## Slide 48: Formulas for Gaussian models
Prior for values.
Uncertainties are timber values.
Likelihood,
design matrix, picks data locations.
Motivation, uncertainties on a grid – forest units.

## Slide 49: Conditioning – Gaussian models
Prediction, Kriging.

## Slide 50: VOI – Gaussian models
Low flexibility:
Must select all units, or none.
standard Gaussian density and cumulative function
Value decouples to sum.

## Slide 51: Results - Forestry example
.
Total: all cells. Partial: Every cell along center lines. Aggregated partial: sums along center lines.
Low flexibility:
Must select all units, or none.
(Results are normalized for area).

## Slide 52: Insight in VOI from this example
.
Total test does not necessarily give much higher VOI than a partial test. It depends on the spatial design of experiment as well as the prior model (mean and dependence).
VOI increases with larger dependence in spatial uncertainties.
VOI is largest when we are most indifferent in prior (mean near 0 and large prior uncertainty.
VOI increases with higher accuracy of measurements.

## Slide 53
Project : Norwegian wood
Consider profits from timber in a forest split in many units. Profits are modeled as a Gaussian random field represented on a 25 x 25 grid for the 625 units. The mean is m=0 at all cells, the covariance is exponential with st dev r=1 and correlation range r=40. Use the code to draw a random realization of this Gaussian process.
One can gather imperfect data at 100 random design locations, giving unbiased profit measurements, and independent error with st dev 0.5. Use the code to draw a random dataset.
Compute the Kriging prediction and the associated variances. See code.
Compute the VOI (using the same data design) of the decision situation where the farmer harvest all units or none.
Compare the VOI results (using the same data design) for different prior mean, variances, correlation ranges and measurement noise terms.